## Slide 1
STATION 509 · ENGINEERING REVIEW
AI_CAM v1.2.1
Production
Stabilization
Industrial AI VIN Reading & Traceability System
One trigger. One body-cycle. One auditable result.
DOCUMENTATION PACKAGE · 29 JULY 2026
Notes: [Sources]
- Repository: README.md; VERSION; config/settings.yaml
- Generated visual: reports/assets/ai_cam_isometric_hero.png (OpenAI ImageGen; no external asset)
[/Sources]

## Slide 2
02
WHY AI_CAM EXISTS
A single body produces multiple identity signals
The production risk is not missing data—it is losing the relationship between signals.
PLC
arrival pulse
defines the cycle
VISION
engraved VIN
reads physical identity
RFID
electronic EPC
reads tag identity
AI_CAM OPERATING CONTRACT
One body-cycle
owns every result.
The session binds trigger, camera frames, YOLO crops, OCR evidence, RFID events, final status, and stored evidence before anything is persisted.
1
accepted trigger
1
body-cycle
1
final row
Notes: [Sources]
- Repository: README.md
- Repository: backend/pipeline.py
- Repository: backend/database/db.py
[/Sources]

## Slide 3
03
END-TO-END WORKFLOW
Every body follows one deterministic evidence path
Camera and RFID start in parallel; the session closes only once.
D2222
ARRIVAL
SESSION
open owner
start 30 s deadline
CAMERA → YOLO
stable VIN crop
RFID INVENTORY
session EPC
3 OCR VIEWS
validate / preserve
SESSION BINDING
VIN + EPC + evidence
FINALIZE ONCE
SQLite row
Dashboard
Logs + evidence
Notes: [Sources]
- Repository: README.md
- Repository: backend/pipeline.py
- Repository: backend/rfid/rfid_service.py
- Repository: backend/database/db.py
[/Sources]

## Slide 4
04
BODY-CYCLE CONTROL
The PLC pulse is a boundary—not just a signal
Debounce and suppression protect the one-body / one-record invariant.
ARMED
zero observed
DEBOUNCE
stable high ≥ 200 ms
ACTIVE
session owns capture
FINALIZE
result or deadline
CLOSED
one row updated
Triggers received while ACTIVE
DUPLICATE IGNORED
EARLY TRIGGER AUDITED
Production queueing is disabled. The next body must rearm through zero and satisfy the minimum interval.
90 s
minimum body interval
Notes: [Sources]
- Repository: config/settings.yaml (plc and session sections)
- Repository: backend/plc/plc_service.py
- Repository: backend/pipeline.py
- Repository: backend/plc/edge_audit.py
[/Sources]

## Slide 5
05
HARDWARE STACK
Four hardware layers anchor the system in the cell
Exact ordering variants and the installed GPU SKU still require commissioning evidence.
SICK
INDUSTRIAL VISION
SICK Lector 652
2.1 MP · 2048×1088 · up to 70 Hz
GigE / IP65 family
CoLa 2111 + project BLOB 2113
MELS
LINE CONTROLLER
MELSEC-Q
MC protocol · D register · 3E frame
D2222 bit 0
100 ms polling / 200 ms debounce
IMPI
RAIN RFID
Impinj R700
4 ports · ISO 18000-63 · up to 1100 reads/s
REST + HTTP stream
session-window RSSI selection
NVID
EDGE INFERENCE
NVIDIA target
cuda:0 target · safe CPU fallback
Installed model unresolved
Torch + Paddle probes required
FAMILY-LEVEL CAPABILITIES · LIVE SKU / FIRMWARE / OPTICS / ANTENNAS / GPU TO BE CAPTURED ON SITE
Notes: [Sources]
- Repository: reports/HARDWARE_CAPABILITY_REPORT.md
- SICK official operating instructions: https://cdn.sick.com/media/docs/3/53/453/operating_instructions_lector64x_65x_flex_lector65x_dynamic_focus_fr_im0071453.pdf
- Mitsubishi official MC Protocol manual: https://www.mitsubishielectric.com/dl/fa/document/manual/plc/sh080008/sh080008ab.pdf
- Impinj R700 official datasheet: https://support.impinj.com/hc/article_attachments/31243539924371
- NVIDIA model is not asserted; README.md uses GTX 1650 only as an example
[/Sources]

## Slide 6
06
VISION PIPELINE
Vision starts by finding the right metal region
A high-quality crop cannot bypass low detector confidence.
DECODED FRAME
VIN REGION
Illustrative schematic — no runtime images are packaged in this release
01
SICK frame
CoLa control + BLOB payload
02
YOLO box
local models/yolo/best.pt
03
Stable evidence
multi-frame / IoU / quality
04
OCR submit
peak YOLO ≥ 0.90
STRICT GATE
0.90
minimum peak YOLO
confidence before OCR
Notes: [Sources]
- Repository: backend/camera/camera_client.py
- Repository: backend/ai/detector.py
- Repository: backend/pipeline.py (_submit_ocr_frames)
- Repository: backend/config.py (ocr_submit_min_yolo_conf default)
[/Sources]

## Slide 7
07
AI STACK
Parallel OCR views expose single-model blind spots
The production VIN comes from Paddle variant fusion; the three-engine stage preserves additional evidence.
SHARED INPUT
VIN CROP
one session · one source
EVIDENCE CANDIDATE
ENGRAVED_V121
ONNX/PT engraved-character classifier
adaptive segmentation · per-character gates
EVIDENCE VALIDATOR
PADDLE_RAW
raw / minimally normalized crop
preserves an independent OCR payload
EVIDENCE VALIDATOR
PADDLE_ENHANCED
contrast-enhanced crop
separate inference and stored payload
CURRENT LIVE AUTHORITY: process-isolated multi-crop Paddle variants + position-level VIN fusion
Notes: [Sources]
- Repository: docs/OCR_FUSION.md
- Repository: backend/ai/ocr_orchestrator.py
- Repository: backend/ai/engines/engraved_v121.py
- Repository: backend/ai/engines/paddle_profiles.py
- Repository: backend/database/ocr_v121_db.py
[/Sources]

## Slide 8
08
OCR DECISION LOGIC
The production VIN is a guarded Paddle fusion result
Parallel Engraved/RAW/Enhanced output explains disagreement but does not currently write the session VIN.
1
READ
multi-crop Paddle preprocessing variants
2
FUSE
weighted character votes by position
3
APPLY
known-model rules + auditable corrections
4
GATE
score · margins · support · conflicts
5
LOCK
accepted VIN becomes immutable
Configuration / implementation reconciliation required
YAML: GUARDED_PRIMARY
Call graph: write_final = false
The evidence-stage candidate is stored for audit/collection; OCRWorker remains the body-cycle authority.
Notes: [Sources]
- Repository: config/settings.yaml (ocr_release.release_mode)
- Repository: RELEASE_NOTES_v1.2.1.md
- Repository: README.md
- Repository: backend/config.py
- Repository: backend/ai/ocr_orchestrator.py
[/Sources]

## Slide 9
09
REAL OCR CHALLENGE
Weak characters expose the next validation gap
Engraved metal, glare, perspective, and narrow strokes make some glyphs systematically confusable.
SCHEMATIC EVIDENCE STRIP
··· U / V ··· F / E ··· 0 / 6 / 8 ···
No runtime crops or production VINs are included in this release tree.
Implemented helper proposes:
≥ 2 independent frames
OR ≥ 2 engines agree
OR high engraved character confidence
SOURCE HASH
preprocessing variants can count once
DISAGREEMENT
utilities compare raw / final / engines
LIVE STATUS
helpers are tested but not wired to acceptance
Notes: [Sources]
- Repository: backend/ai/ocr_disagreement.py
- Repository: docs/OCR_FUSION.md
- Repository asset boundary: runtime/crops contains only .gitkeep in this release
[/Sources]

## Slide 10
10
MODEL IMPROVEMENT LOOP
Every hard case can improve the next model
The current live loop generates review candidates—not automatic ground truth.
AMBIGUOUS
no-read / disagreement / weak char
CAPTURE
source frame + line + engine evidence
ALIGN
engine boxes or projection valleys
REVIEW
authoritative or human approval
TRAIN
versioned dataset and evaluation
Why equal-width splitting is blocked
Perspective + uneven engraving + padding + narrow/wide glyphs can cut through strokes.
EQUAL SPLIT = PENDING REVIEW
Collector metadata blocks equal-split training; SQLite eligibility fields still need schema parity
Notes: [Sources]
- Repository: docs/DATASET_CHARACTER_ALIGNMENT.md
- Repository: backend/ai/ocr_collector.py
- Repository: backend/ai/dataset_collector.py
- Repository: tests/test_dataset_alignment_v13.py
[/Sources]

## Slide 11
11
SOFTWARE ARCHITECTURE
Session ownership keeps parallel results attached
Device I/O, AI inference, persistence, and UI share one explicit session identity.
PLC SERVICE
CAMERA CLIENT
RFID SERVICE
STATE OWNER
PIPELINE
session map
capture owner
deadlines · retries
finalization
YOLO + OCR
SQLITE
LOGS / AUDIT
FASTAPI
REST
MJPEG
Dashboard
History
Notes: [Sources]
- Repository: backend/pipeline.py
- Repository: backend/server.py
- Repository: backend/ai/detector.py and backend/ai/ocr_worker.py
- Repository: backend/database/db.py
- Repository: frontend/templates and frontend/static
[/Sources]

## Slide 12
12
PERSISTENCE AND TRACEABILITY
One session becomes one auditable database row
Three OCR engine rows explain the decision without multiplying production records.
SESSION START
INSERT pending row
vin_records
UNIQUE session_id
VIN · raw OCR · model · confidence
RFID EPC + raw EPC · status · image
failure reason · latency · timestamps
ocr_engine_results
one row per engine / session
text · boxes · confidence · model · latency · errors
ocr_collection_items
alignment · label status · review metadata
FINALIZATION UPDATES THE SAME ROW
Notes: [Sources]
- Repository: backend/database/db.py
- Repository: backend/database/ocr_v121_db.py
- Repository: migrations/v1_2_1_ocr_evidence.sql
[/Sources]

## Slide 13
13
OPERATOR EXPERIENCE
Operators see live evidence and history
The schematic is reconstructed from the actual templates and API—not presented as a screenshot.
AI_CAM / DASHBOARD
CAMERA
READY
PLC
READY
RFID
READY
AI
READY
LAST VIN
—
LIVE MJPEG / YOLO OVERLAY
camera frame area
PLC CONTROL
ON / OFF
COUNTERS
FPS · DET · VIN
DASHBOARD
device state · live stream · counters
HISTORY
VIN/RFID filter · status · image · export
LOGS
search · stream · stats · download
SYSTEM
health · services · architecture
SETTINGS
masked secrets · controlled updates
Notes: [Sources]
- Repository: frontend/templates/dashboard.html
- Repository: frontend/templates/history.html
- Repository: frontend/templates/logs.html, system.html, settings.html
- Repository: backend/server.py
- Repository: frontend/static/js/dashboard.js and history.js
[/Sources]

## Slide 14
14
PRODUCTION STABILIZATION
Stabilization closes the failure loops
The release adds bounded behavior and evidence at the exact points where production ambiguity occurs.
TRIGGER
edge debounce
suppression audit
CAPTURE
watchdog
reconnect / ownership
DETECTION
stable frames
strict 0.90 OCR gate
OCR
new-evidence retry
VIN_LOCKED
FAILURE
best crop / last frame
reasoned status
OBSERVE
24 h real artifacts
honesty gate
DECODED FRAMES + NO VIN ⇒ EVIDENCE IMAGE · PARTIAL OBSERVATION ⇒ NOT COMPLETED
Notes: [Sources]
- Repository: CHANGELOG.md
- Repository: docs/FAILURE_EVIDENCE.md
- Repository: docs/PRODUCTION_OBSERVATION.md
- Repository: backend/ai/ocr_retry_guard.py
- Repository: backend/plc/edge_audit.py
[/Sources]

## Slide 15
15
CODEBASE STRUCTURE
Devices, AI, data, and operations stay separated
The pipeline integrates adapters; tests keep subsystem behavior explicit.
backend/pipeline.py
Session state
Device coordination
Capture + inference ownership
Finalization
backend/plc
trigger + audit
backend/camera
CoLa + BLOB
backend/rfid
R700 + EPC
backend/ai
YOLO + OCR + collection
backend/database
SQLite + migration
backend/server + frontend
API + operator UI
run.py · config/settings.yaml · models/ · tests/ · tools/ · docs/ · reports/
Notes: [Sources]
- Repository: run.py
- Repository: backend/ and frontend/
- Repository: reports/SYSTEM_DISCOVERY_REPORT.md
- Repository: reports/CODE_ARCHITECTURE_ANALYSIS.md
[/Sources]

## Slide 16
16
ENGINEERING ASSESSMENT
Current strengths are clear; remaining gates are operational
The architecture is evidence-rich, but live cell proof still determines production confidence.
CURRENT STRENGTHS
✓
Explicit session ownership
✓
One-record idempotency
✓
Per-engine evidence beside production Paddle fusion
✓
Bounded retries + VIN lock
✓
Failure image preservation
✓
Portable local models and runtime
OPEN GATES
!
Reconcile GUARDED_PRIMARY config vs evidence-only hook
!
Verify camera optics and real VIN image quality
!
Confirm PLC module, port, and ladder pulse
!
Validate R700 region / antennas / RF field
!
Capture exact GPU and CUDA framework readiness
!
Integrate weak-character guards and complete 24 h observation
Notes: [Sources]
- Repository: reports/CODE_ARCHITECTURE_ANALYSIS.md
- Repository: reports/HARDWARE_CAPABILITY_REPORT.md
- Repository: reports/FINAL_RELEASE_CONSOLIDATION_REPORT.md
- Repository: docs/PRODUCTION_OBSERVATION.md
[/Sources]

## Slide 17
17
READINESS GATE
Commissioning evidence determines readiness
Offline coverage supports deployment; it does not replace proof from Station 509.
01
PLC
one pulse → one session
no replay / no duplicate
02
CAMERA
nameplate + optics
capture / reconnect / exposure
03
RFID
region + firmware + antennas
adjacent-body / stale-tag test
04
GPU
exact SKU + driver
Torch and Paddle CUDA probes
05
24 H
real window completed
zero duplicate records
Documentation package: READY
Live production validation: PENDING SITE EVIDENCE
Notes: [Sources]
- Repository: reports/HARDWARE_CAPABILITY_REPORT.md (live validation checklist)
- Repository: reports/FINAL_RELEASE_CONSOLIDATION_REPORT.md
- Repository: docs/HIL_PRODUCTION_VALIDATION_PLAN.md
- Repository: docs/PRODUCTION_OBSERVATION.md
[/Sources]

## Slide 18
AI_CAM V1.2.1
One trigger.
One body.
One traceable result.
AI_CAM turns a PLC event, engraved identity, and RFID evidence into a single session-owned production record—with the data needed to explain success and failure.
PLC
VISION
RFID
RECORD
NEXT: CAPTURE SITE EVIDENCE · ALIGN OCR AUTHORITY · COMPLETE 24-HOUR OBSERVATION
Notes: [Sources]
- Repository: README.md
- Repository: reports/CODE_ARCHITECTURE_ANALYSIS.md
- Repository: reports/HARDWARE_CAPABILITY_REPORT.md
[/Sources]